## Slide 1: Chapter 9: Main Memory

## Slide 2: Chapter 9: Memory Management
Background
Contiguous Memory Allocation
Paging
Structure of the Page Table
Swapping
Example: The Intel 32 and 64-bit Architectures
Example: ARMv8 Architecture

## Slide 3: Background
Program must be brought (from disk) into memory and placed within a process for it to be run
Main memory and registers are only storage CPU can access directly
Memory unit only sees a stream of:
  addresses + read requests, or
  address + data and write requests
Register access is done in one CPU clock (or less)
Main memory can take many cycles, causing a stall
Cache sits between main memory and CPU registers
Protection of memory required to ensure correct operation

## Slide 4: Protection
Need to censure that a process can access only those addresses in its address space.
We can provide this protection by using a pair of base and limit registers define the logical address space of a process

## Slide 5: Hardware Address Protection
CPU must check every memory access generated in user mode to be sure it is between base and limit for that user
the instructions to loading the base and limit registers are privileged

## Slide 6: Contiguous Allocation
Main memory must support both OS and user processes
Limited resource, must allocate efficiently
Contiguous allocation is one early method
Main memory usually into two partitions:
  Resident operating system, usually held in low memory with interrupt vector
  User processes then held in high memory
  Each process contained in single contiguous section of memory

## Slide 7: Contiguous Allocation (Cont.)
Relocation registers used to protect user processes from each other, and from changing operating-system code and data
  Base register contains value of smallest physical address
  Limit register contains range of logical addresses – each logical address must be less than the limit register
  MMU maps logical address dynamically
  Can then allow actions such as kernel code being transient and kernel changing size

## Slide 8: Variable Partition
Multiple-partition allocation
  Degree of multiprogramming limited by number of partitions
  Variable-partition sizes for efficiency (sized to a given process’ needs)
  Hole – block of available memory; holes of various size are scattered throughout memory
  When a process arrives, it is allocated memory from a hole large enough to accommodate it
  Process exiting frees its partition, adjacent free partitions combined
  Operating system maintains information about: a) allocated partitions b) free partitions (hole)

## Slide 9: Dynamic Storage-Allocation Problem
First-fit: Allocate the first hole that is big enough
Best-fit: Allocate the smallest hole that is big enough; must search entire list, unless ordered by size
  Produces the smallest leftover hole
Worst-fit: Allocate the largest hole; must also search entire list
  Produces the largest leftover hole
How to satisfy a request of size n from a list of free holes?
First-fit and best-fit better than worst-fit in terms of speed and storage utilization

## Slide 10: Fragmentation
External Fragmentation – total memory space exists to satisfy a request, but it is not contiguous
Internal Fragmentation – allocated memory may be slightly larger than requested memory; this size difference is memory internal to a partition, but not being used
First fit analysis reveals that given N blocks allocated, 0.5 N blocks lost to fragmentation
  1/3 may be unusable -> 50-percent rule

## Slide 11: Fragmentation (Cont.)
Reduce external fragmentation by compaction
  Shuffle memory contents to place all free memory together in one large block
  Compaction is possible only if relocation is dynamic, and is done at execution time
  I/O problem
    Latch job in memory while it is involved in I/O
    Do I/O only into OS buffers
Now consider that backing store has same fragmentation problems

## Slide 12: Paging
Physical address space of a process can be noncontiguous; process is allocated physical memory whenever the latter is available
  Avoids external fragmentation
  Avoids problem of varying sized memory chunks
Divide physical memory into fixed-sized blocks called frames
  Size is power of 2, between 512 bytes and 16 Mbytes
Divide logical memory into blocks of same size called pages
Keep track of all free frames
To run a program of size N pages, need to find N free frames and load program
Set up a page table to translate logical to physical addresses
Backing store likewise split into pages
Still have Internal fragmentation

## Slide 13: Address Translation Scheme
Address generated by CPU is divided into:
  Page number (p) – used as an index into a page table which contains base address of each page in physical memory
  Page offset (d) – combined with base address to define the physical memory address that is sent to the memory unit
  For given logical address space 2m and page size 2n

## Slide 14: Paging Model of Logical and Physical Memory

## Slide 15: Paging Example
Logical address: n = 2 and m = 4. Using a page size of 4 bytes and a physical memory of 32 bytes (8 pages)

## Slide 16: Paging -- Calculating internal fragmentation
Page size = 2,048 bytes
Process size = 72,766 bytes
35 pages + 1,086 bytes
Internal fragmentation of 2,048 - 1,086 = 962 bytes
Worst case fragmentation = 1 frame – 1 byte
On average fragmentation = 1 / 2 frame size
So small frame sizes desirable?
But each page table entry takes memory to track
Page sizes growing over time
  Solaris supports two page sizes – 8 KB and 4 MB

## Slide 17: Free Frames
Before allocation
After allocation

## Slide 18: Implementation of Page Table
Page table is kept in main memory
  Page-table base register (PTBR) points to the page table
  Page-table length register (PTLR) indicates size of the page table
In this scheme every data/instruction access requires two memory accesses
  One for the page table and one for the data / instruction
The two-memory access problem can be solved by the use of a special fast-lookup hardware cache called translation look-aside buffers (TLBs) (also called associative memory).

## Slide 19: Translation Look-Aside Buffer
Some TLBs store address-space identifiers (ASIDs) in each TLB entry – uniquely identifies each process to provide address-space protection for that process
  Otherwise need to flush at every context switch
TLBs typically small (64 to 1,024 entries)
On a TLB miss, value is loaded into the TLB for faster access next time
  Replacement policies must be considered
  Some entries can be wired down for permanent fast access

## Slide 20: Effective Access Time
  Hit ratio – percentage of times that a page number is found in the TLB
An 80% hit ratio means that we find the desired page number in the TLB 80% of the time.
Suppose that 10 nanoseconds to access memory.
  If we find the desired page in TLB then a mapped-memory access take 10 ns
  Otherwise we need two memory access so it is 20 ns
Effective Access Time (EAT)
EAT = 0.80 x 10 + 0.20 x 20 = 12 nanoseconds
implying 20% slowdown in access time
Consider amore realistic hit ratio of 99%,
  EAT = 0.99 x 10 + 0.01 x 20 = 10.1ns
implying only 1% slowdown in access time.

## Slide 21: Memory Protection
Memory protection implemented by associating protection bit with each frame to indicate if read-only or read-write access is allowed
  Can also add more bits to indicate page execute-only, and so on
Valid-invalid bit attached to each entry in the page table:
  “valid” indicates that the associated page is in the process’ logical address space, and is thus a legal page
  “invalid” indicates that the page is not in the process’ logical address space
  Or use page-table length register (PTLR)
Any violations result in a trap to the kernel

## Slide 22: Valid (v) or Invalid (i) Bit In A Page Table

## Slide 23: Shared Pages
Shared code
  One copy of read-only (reentrant) code shared among processes (i.e., text editors, compilers, window systems)
  Similar to multiple threads sharing the same process space
  Also useful for interprocess communication if sharing of read-write pages is allowed
Private code and data
  Each process keeps a separate copy of the code and data
  The pages for the private code and data can appear anywhere in the logical address space

## Slide 24: Shared Pages Example

## Slide 25: Structure of the Page Table
Memory structures for paging can get huge using straight-forward methods
  Consider a 32-bit logical address space as on modern computers
  Page size of 4 KB (212)
  Page table would have 1 million entries (232 / 212)
  If each entry is 4 bytes  each process 4 MB of physical address space for the page table alone
    Don’t want to allocate that contiguously in main memory
  One simple solution is to divide the page table into smaller units
    Hierarchical Paging
    Hashed Page Tables
    Inverted Page Tables

## Slide 26: Hierarchical Page Tables
Break up the logical address space into multiple page tables
A simple technique is a two-level page table
We then page the page table

## Slide 27: Two-Level Paging Example
A logical address (on 32-bit machine with 4K page size) is divided into:
  a page number consisting of 20 bits
  a page offset consisting of 12 bits
Since the page table is paged, the page number is further divided into:
  a 10-bit page number
  a 10-bit page offset
Thus, a logical address is as follows:
where p1 is an index into the outer page table, and p2 is the displacement within the page of the inner page table
Known as forward-mapped page table

## Slide 28: Address-Translation Scheme

## Slide 29: 64-bit Logical Address Space
Even two-level paging scheme not sufficient
If page size is 4 KB (212)
  Then page table has 252 entries
  If two level scheme, inner page tables could be 210 4-byte entries
  Address would look like
  Outer page table has 242 entries or 244 bytes
  One solution is to add a 2nd outer page table
  But in the following example the 2nd outer page table is still 234 bytes in size
    And possibly 4 memory access to get to one physical memory location

## Slide 30: Three-level Paging Scheme

## Slide 31: Hashed Page Tables
Common in address spaces > 32 bits
The virtual page number is hashed into a page table
  This page table contains a chain of elements hashing to the same location
Each element contains (1) the virtual page number (2) the value of the mapped page frame (3) a pointer to the next element
Virtual page numbers are compared in this chain searching for a match
  If a match is found, the corresponding physical frame is extracted
Variation for 64-bit addresses is clustered page tables
  Similar to hashed but each entry refers to several pages (such as 16) rather than 1
  Especially useful for sparse address spaces (where memory references are non-contiguous and scattered)

## Slide 32: Hashed Page Table

## Slide 33: Inverted Page Table
Rather than each process having a page table and keeping track of all possible logical pages, track all physical pages
One entry for each real page of memory
Entry consists of the virtual address of the page stored in that real memory location, with information about the process that owns that page
Decreases memory needed to store each page table, but increases time needed to search the table when a page reference occurs
Use hash table to limit the search to one — or at most a few — page-table entries
  TLB can accelerate access
But how to implement shared memory?
  One mapping of a virtual address to the shared physical address

## Slide 34: Inverted Page Table Architecture

## Slide 35: Swapping
A process can be swapped temporarily out of memory to a backing store, and then brought back into memory for continued execution
  Total physical memory space of processes can exceed physical memory
Backing store – fast disk large enough to accommodate copies of all memory images for all users; must provide direct access to these memory images
Roll out, roll in – swapping variant used for priority-based scheduling algorithms; lower-priority process is swapped out so higher-priority process can be loaded and executed
Major part of swap time is transfer time; total transfer time is directly proportional to the amount of memory swapped
System maintains a ready queue of ready-to-run processes which have memory images on disk

## Slide 36: Swapping (Cont.)
Does the swapped out process need to swap back in to same physical addresses?
Depends on address binding method
  Plus consider pending I/O to / from process memory space
Modified versions of swapping are found on many systems (i.e., UNIX, Linux, and Windows)
  Swapping normally disabled
  Started if more than threshold amount of memory allocated
  Disabled again once memory demand reduced below threshold

## Slide 37: Schematic View of Swapping

## Slide 38: Context Switch Time including Swapping
If next processes to be put on CPU is not in memory, need to swap out a process and swap in target process
Context switch time can then be very high
100MB process swapping to hard disk with transfer rate of 50MB/sec
  Swap out time of 2000 ms
  Plus swap in of same sized process
  Total context switch swapping component time of 4000ms (4 seconds)
Can reduce if reduce size of memory swapped – by knowing how much memory really being used
  System calls to inform OS of memory use via request_memory() and release_memory()

## Slide 39: Context Switch Time and Swapping (Cont.)
Other constraints as well on swapping
  Pending I/O – can’t swap out as I/O would occur to wrong process
  Or always transfer I/O to kernel space, then to I/O device
    Known as double buffering, adds overhead
Standard swapping not used in modern operating systems
  But modified version common
    Swap only when free memory extremely low

## Slide 40: Swapping on Mobile Systems
Not typically supported
  Flash memory based
    Small amount of space
    Limited number of write cycles
    Poor throughput between flash memory and CPU on mobile platform
Instead use other methods to free memory if low
  iOS asks apps to voluntarily relinquish allocated memory
    Read-only data thrown out and reloaded from flash if needed
    Failure to free can result in termination
  Android terminates apps if low free memory, but first writes application state to flash for fast restart
  Both OSes support paging as discussed below

## Slide 41: Swapping with Paging

## Slide 42: Example: The Intel 32 and 64-bit Architectures
Dominant industry chips
Pentium CPUs are 32-bit and called IA-32 architecture
Current Intel CPUs are 64-bit and called IA-64 architecture
Many variations in the chips, cover the main ideas here

## Slide 43: Example: The Intel IA-32 Architecture
Supports both segmentation and segmentation with paging
  Each segment can be 4 GB
  Up to 16 K segments per process
  Divided into two partitions
    First partition of up to 8 K segments are private to process (kept in local descriptor table (LDT))
    Second partition of up to 8K segments shared among all processes (kept in global descriptor table (GDT))

## Slide 44: Example: The Intel IA-32 Architecture (Cont.)
CPU generates logical address
  Selector given to segmentation unit
    Which produces linear addresses
  Linear address given to paging unit
    Which generates physical address in main memory
    Paging units form equivalent of MMU
    Pages sizes can be 4 KB or 4 MB

## Slide 45: Logical to Physical Address Translation in IA-32

## Slide 46: Intel IA-32 Paging Architecture

## Slide 47: Intel x86-64
Current generation Intel x86 architecture
64 bits is ginormous (> 16 exabytes)
In practice only implement 48 bit addressing
  Page sizes of 4 KB, 2 MB, 1 GB
  Four levels of paging hierarchy
Can also use PAE so virtual addresses are 48 bits and physical addresses are 52 bits

## Slide 48: End of Chapter 9